## Slide 1
AIRSPACES : Aerial Imaging and Remote Sensing for Precision Agriculture and Environmental Stewardship
Abhijit Nagchaudhuri, Ph.D., Professor(Engineering)
Dept. of Engineering and Aviation Sciences
University of Maryland Eastern Shore
UMES Collaborators : Dr. Madhumi Mitra , Dr. Lurline Marsh
and Dr. Jurgen Schwarz ( School of Agriculture and Natural Sciences), Christopher Hartman ( Aviation Coordinator)
External Collaborators : USDA, NASA, Pioneer Hi-Bred Int.
Support : UMES STEAM students , GIS Pgm Mgr, and farm personnel
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH

## Slide 2
REMOTE SENSING
Remote Sensing is a broad field encompassing approaches to extract information about objects without coming into physical contact with them.
Remote sensing is broadly classified as passive, where the sensing system acquires information from the solar reflectance or electromagnetic emission from objects (e.g., ETM) and active, where the sensing system provides its own source of directed radiation and captures reflectance or backscattering of the radiation from the target objects (e.g., RADAR).
http://www.laserveil.com
/radar/jammers/
http://www.aokc.net/latest-news
Credit : Hubble ( Space Telescope Science Institute)
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH

## Slide 3
REMOTE SENSING
Remote sensing is widely utilized by scientists and engineers in space and earth sciences, medical sciences, agriculture, various applications in the industry, and social sciences.
https://geo.arc.nasa.gov/sge/landsat/l7image.html
http://landsat.gsfc.nasa.gov/?p=3186

## Slide 4
Robotics and Mechatronics Laboratory(UMES)
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH
Nagchaudhuri, A., Kuruganty, S., and Shakur, A., “Introduction to Mechatronics Concepts in a Robotics Course using an Industrial SCARA Robot and Integrated Vision System”, Mechatronics ( Elsevier Science Ltd.)Vol. 12, 2002, pp. 183-193.

## Slide 5
REMOTE SENSING AT UMES - INITIAL PHASE
- Blimp
7 foot dia.
21 foot length
16 lb. lift
Gondola-7 lb.(max) (includes all components) Detachable from blimp
2.4 GHz transmitters,
4-Channel simultaneous
( Upto 2500 ft.)
Nagchaudhuri, A., and Bland, G., 2002. "UMES-AIR: A NASA-UMES Collaborative Project to Promote Experiential Learning & Research in Multidisciplinary Teams for SMET Students", Journal of SMET Education: Innovations and Research. Jul –Dec
UMESAIR :Undergraduate Multidisciplinary Earth Science
Airborne Instrumentation Research

## Slide 6: What is precision agriculture? Environmentally Conscious Precision Agriculture – A Platform for Active Learning and Community Engagement
Precision Agriculture involves optimizing inputs and monitoring outputs of an agricultural system at as high a spatial resolution as possible to improve profits and minimize environmental impact.
Also called
  Site Specific Management (SSM)
  Precision Farming (PF)
  Precision Crop Management (PCM)
Simple definition
  Right Input
  Right product
  Right time
  Right place
http://blog.farmorganix.com/wpcontent/uploads/2013/01/Precision_Farming.jpg

## Slide 7
Ground Based Data
Leaf Area Index LAI2000
Average height
NDVI/ Greenseeker Chlorophyll contentSPAD502
Remotely Sensed Data
Terra Hawk aerial imaging
Kite aerial imaging
Final harvest via Yield Monitoring
Plant density count
Various Aspects of Field Experiments ( General Overview)
UMES ECPA/ AIRSPACES Projects - Pictorial Overview (2006-2011)
R/C Models with Camera
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH
Henry, X., Nagchaudhuri, A., Mitra, M., and Marsh, L., 2013. “Using Variable Rate Seeding and Remote Sensing Technologies to Optimize Corn Yield and Profit on a Farm with Non-Uniform Productivity”, International Journal of Applied Agricultural Research, Vol. 8, No:2, 2013, pp. 187-200.

## Slide 8
AIRSPACES2
Aerial Imaging and Remote Sensing for Precision Agriculture and Environmental Stewardship
Air-propelled Instrumented Robotic Sensory Platform for Assateague Coastline Environmental Studies

## Slide 9
RC-UAVS-GEOREFERENCING and MOSAICKING ( Early Efforts)
Software tools : Multispec, ARCGIS,SMS, and MATLAB

## Slide 10
Remote Sensing and Yield Map ( Early Efforts)
Bozman
Bozman -Corn
Aerial images do not have enough resolution to capture the low levels of yield variation observed from the yield monitor data
Example: Unable to see vertical line of poor yielding area
(http://pubs.ext.vt.edu/442/442-502/L_44250201.jpg)

## Slide 11: Overview

## Slide 12: EMPHASIS ON DEFENSE (PEOPLE – PLANET- PROFIT)
D D - Disease Prevention
E - Energy
F - Food
E - Environment
NS - National Security
E - Education
- Disease Prevention
E - Energy
F - Food
E - Environment
NS - National Security
E - Education
Precision Agriculture : Turning Swords into Ploughshare
The phrase “the triple bottom line” was first coined in 1994 by John Elkington, the founder of a British consultancy called SustainAbility.
Precision Agriculture : Turning Swords into Ploughshare
D - Disease Prevention
E - Energy
F - Food
E - Environment
NS - National Security
E - Education

## Slide 13
,
MULTISPECTRAL REMOTE SENSING CAPABILITIES AT UMES : Cessna 172 (Manned)

## Slide 14
,
MULTISPECTRAL REMOTE SENSING-CESSNA172- TERRAHAWK- UMES-FIELD EXPERIMENT (Manned

## Slide 15
,
The ADC Lite contains a single 3.2 megapixel Complementary Metal Oxide Semiconductor (CMOS) sensor ( single array with Bayer pattern filters) optimized for capture of visible light wavelengths longer than 520 nm and near-infrared wavelengths up to 920 nm.
MULTISPECTRAL REMOTE SENSING CAPABILITIES AT UMES ( Tetracam)
KITES/UAVS
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH

## Slide 16
,
MULTISPECTRAL REMOTE SENSING- KITE- UMES-FIELD EXPERIMENT

## Slide 17: Applied Research Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing, and Drought Tolerant Corn Seeds (2012 -2015) ( NIFA : CBG)
http://www.engineeringchallenges.org/

## Slide 18: Applied Research and Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing and Drought Tolerant Corn Seeds (2012-2015)

## Slide 19
PMT, GRID SOIL SAMPLING – SOIL TEST RESULTS ON GIS MAP ( BOZMAN FIELD)
WICKED PROBLEM – EASTERN SHORE
Batie, 2008
PMT delays could outlast O’Malley administration
By BRUCE HOTCHKISS Senior Editor (July 1, 2014) Even as an ……

## Slide 20: “Not so Remote Sensing” Optical sensors – Crop Health- (CIR) Color InfraRed Digital Camera
http://agribotix.com/
http://agrielectronics.blogspot.com/2013/
Individual OptRx Active Sensor
OptRx sensors are active sensors that can shine light centered on 670nm (red), 730nm (red_edge) and 780 nm (near-infrared) wavelengths and record reflectance from the crop canopy to determine VIs (vegetation indices) such as NDVI ( ) and NDRE ( indicative of crop biomass and nutrient stress.

## Slide 21
Sensed NDRE (left) and Applied N maps (right) - Ag Leader SMS software
VARIABLE RATE NITROGEN APPLICATION – FIELD TRIAL ( 2013)

## Slide 22: Applied Research and Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing and Drought Tolerant Corn Seeds(2012-2015)
6 Rows, 108 Plots
  15ft x 50ft, 26” bt. Rows
3 factors (6 levels of Nitrogen)
2 seed types
Odd: regular seed
Even: AquaMax
( Drought Tolerant)
3 irrigation levels (rainfed, fully irrigated, partial season irrigation)
FIELD EXPERIMENTS
Experimental ( 2 acre)
  Seed, Irrigation, Fertilizer
Rest of Bozman (40 ac)
  Mid, Early, Late planting
  Seed ( regular and Aquamax)
Presidential field (15 ac)
  Density(24k, 28k, 32k seeds/acre)
  Seed (regular and Aquamax)
Nagchaudhuri, A., et, al ( 2014) “Towards Greener Farms and Cleaner Bays in the Eastern Shore”, Paper number 141913243, Proceedings of 2014 ASABE, \

## Slide 23
Applied Research and Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing and Drought Tolerant Corn Seeds(2013)
Measurements
Soil Nutrient
Content
  Growth Stage
  Height
  SPAD
  Reflectance
  Thermal Temperature
  Soil Moisture
  Yield

## Slide 24: 3DRobotics X8
FAA COA approved July 1, 2014
3DRobotics X8 with Tetracam ADC Lite
Series of test flights with first data acquisition on July 10

## Slide 25: Mission Planner
Applied Research and Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing and Drought Tolerant Corn Seeds(2014)- UAV Remote Sensing (Mission Planner)
3DRX8 - Mission ( UAV Flight Movie)

## Slide 26: Applied Research and Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing and Drought Tolerant Corn Seeds(2014)- UAV Remote Sensing
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH

## Slide 27
Applied Research and Field Experiments utilizing Variable Rate Nitrogen Application, Remote and In Situ Sensing and Drought Tolerant Corn Seeds(2014)- UAV Remote Sensing
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH
Hartman, C., Nagchaudhuri,A., Mitra,M., and Daughtry,C.,(2014)"The development of Nitrogen response curves for the improvement of Nitrogen use efficiency (NUE) on Maryland’s Eastern Shore " Paper number 141900381, Proceedings of 2014 ASABE \

## Slide 28: Acknowledgements
NIFA-USDA Capacity Building Grant
Maryland Space Grant Consortium /NASA
Dr. John Moisan,Geoff Bland ,and Ted Miles of NASA
Dr. Craig Daughtry of USDA Beltsville
UMES Students and Farm Personnel

## Slide 29: Questions/Comments/Suggestions
8th International IPM Symposium | MARCH 23–26, 2015 | SALT LAKE CITY, UTAH